## Slide 1: MEG実験アップグレードに向けたMPPC読み出しによる 新しいタイミングカウンターの研究開発
西村美紀 (東大ICEPP)
松本悟、宮崎陽平(九大)
他 MEGコラボレーション
日本物理学会 2012年秋季大会
京都産業大学

## Slide 2: outline
Introduction
  MEG
  Upgrade
Pixelated timing counter
  Concept and expected performance
Single pixel study
  Test with smaller counter
  Construction and test of prototype of single pixel
Summary and Prospects

## Slide 3: μ → eγ
Search for charged lepton flavor violation (cLFV), μ eγ
  Forbidden in the SM
  Some models predict large branching ratios
Event Signature
  : 52.8 MeV
  Gamma-ray : 52.8 MeV
  Time coincidence
  Back-to-back
Background
  Accidental background by Michel positron and gamma-ray ->dominant
Requirement
  high intensity DC beam
  high rate tolerable positron detector
  high performance gamma-ray detector
the upper limit of
SUSY-Seesaw
SUSY-GUT SO(10)
L.Calibbi et al, JHEP 0912:057 (2009)
S.Antusch et al, JHEP 0611:090 (2006)

## Slide 4: MEG
μ beam at PSI (Paul Scherrer Institute)
-> a muon stopping rate of Hz
900L LXe gamma detector
Positron spectrometer
  COBRA
    Gradient magnetic field
    -> sweep the positron out of the detector quickly
    the same momentum
    -> the same radius
  Drift chamber
    Momentum, decay vertex, emission angle and track length
  Timing counter
    Impact time
Most stringent upper limit of in summer 2011
Sensitivity goal -> ~ in 2013

## Slide 5: Upgrade
sensitivity goal ->
  Improve detection efficiency
  Improve resolutions
  -> Background reduction
μ beam
    a higher beam intensity
Xenon Calorimeter
    Smaller photo-sensor
Positron spectrometer
  Positron tracker
    efficiency
    ->minimize material along the positrons
    path to the timing counter
    Resolution
    ->increase measurement points
    Stereo wire drift chamber
    Time projection chamber (TPC)
  Timing counter
    Pixelated Timing Counter
Timing counter
Positron Tracker
present
upgrade
2 option

## Slide 6: Pixelated Timing Counter
60
5
30
  (still to be optimized)
Ultra-fast Plastic Scintillator
Composed of several hundreds of small scintillator plates with MPPC readout
  A good timing resolution of single pixel
  -> already proved by the μSR group at PSI
  Using multiple hit time
  Less pileup
  Additional track information
  Insensitivity to magnetic field
  Operational in helium gas (with which COBRA is filled)
  Flexible detector layout
90cm
30cm
-> Readout by waveform digitizer
(DRS developed at PSI)
~400 pixels
present
upgrade
PMT
Scintillator
(upstream, downstream side)

## Slide 7: Expected Performance
Single pixel counter
  μSR counter
  (12x25x5, BC422: attenuation length~8cm, rise time 0.35ns)
(measured)
( photon-sensor coverage)
  MEG design
  (30x60x5, BC418: attenuation length ~100cm, rise time 0.5ns)
(MC) (->45ps)
Multiple hit
⇒ the average time resolution :
30-35 ps (60% ↓)
resolution
130 ps → 80 ps (40% ↓)
track length: 75 ps→ 11 ps
gamma side: 67 ps
Timing counter: 76ps → 30-35ps
# of hit counter (MC)
# of hit counter dependence
(current TC ~76ps)

## Slide 8: Issues
Prove the performance for our application
Larger single counter
Readout system (cabling, electronics…)
Multiple hit principle
Other Possible Issues
Temperature coefficient of MPPC gain
The number of electronics channels (~ 800 pixels × 2 readout) and MPPCs (~ 800 pixels × 6)
Radiation hardness of MPPC
Today’s topic
Test with smaller counter (working at PSI μSR facility)
  Basic performance measurement
  Test of waveform digitizer readout
  Effect of parallel connection
Construction and test of prototype of single pixel

## Slide 9: Single pixel counter study

## Slide 10: Set up
(≒BC422)
2 MPPCs
Series connection
Test counter from μSR group
Reference counter
  5×5×5 mm
  Readout by a MPPC
  -> collimate β-ray, scan position
  trigger
Source Sr90 (~2MeV,β-ray)
Bias 140V~144V (~5.0μA)
Voltage preamp developed by PSI
Waveform digitizer sampling (DRS developed at PSI)
sampling rate -> 5GHz
A. Stoykov et al. NDIP 2011
HV source
Hamamatsu Photonics MPPC S10362-33-050C
KEITHLEY
6487 PICOAMMETER/VOLTAGE SOURCE
HV source
Test counter
Reference counter
HV source
HV source

## Slide 11: analysis
Timing measurement:
average from both sides
Digital Constant Fraction
-> 8%, delay 2ns
Correction by the ratio each side charge and the reference charge
CF
raw

## Slide 12: Intrinsic Resolution
μSR group (TDC)
→
(12x25x5mm EJ232 uniform irradiated)
(smaller counter φ6x0.3mm EJ232)
With waveform digitizer, the good timing resolution is obtained.
Timing resolution scales as square root of Npe
(measured)

## Slide 13: MPPC bias dependence
Good resolution can be obtained stably over certain voltage.
Shift of the timing depending on bias voltage
(-> temperature variation could affect the timing performance)
~100ps/V
44ps

## Slide 14: Temperature stability
The temperature coefficient of the breakdown voltage: 56mV/℃
-> gain variation: 5.6 %/℃
at overvoltage of 1V
(Hamamatsu MPPC S10931-050P)
In the COBRA, temperature changes 2-3℃ -> ~150mV -> ~15ps
Possible solutions
Improve temperature control of detector hut
SiPM with smaller temperature coefficient
->KETEK SiPM (PM3350)
gain variation: <1 %/℃
PhotoDet 2012, June 13-15, 2012, LAL Orsay, France

## Slide 15: Parallel connection
connect outputs in parallel from two pixels located apart from each other
(Low pile up makes it possible.)
Channel reduction
Issues
  Can not give bias voltage each counter
->Choose pairs of the same breakdown voltage
  Capacitance ↑
  ->Change waveform, smaller signal
Though resolution becomes worse because of wave height decrease,
it does NOT change under higher over voltage.

## Slide 16: Pixel prototype
60
4.5
30
Ultra-fast Plastic Scintillator
30×60×4.5 mm scintillator
Two types of scintillators
  BC422: attenuation length 8cm
  rise time 0.35ns
  EJ228: attenuation length 100cm
  rise time 0.5ns
3 MPPCs each side
MPPC: 3×3mm, 50μm pixel pitch
No wrapping (only total reflection)
Optical coupling with optical grease (OKEN6262A)
Expected performance
  BC422 50.1
  EJ228 44.7
Prototype counter
Design of the single pixel module
Three MPPCs on the PCB

## Slide 17: First test with prototype
EJ228
Moving-average 3 points, ARC Constant-fraction with 3.5 ns delay and 8% fraction
1cm
1cm
counter
BC422
Moving-average 3 points, digital Constant-fraction at 8% fraction
Average 53.4 ps
25ps
40ps
53.3 ps
(expected 50.1)
54.8ps
(expected 44.7)
Average 55.4 ps
Resolution doesn’t change so much.
Mean has a little position dependence .
Measured resolution is worse than expected one.
-> We couldn’t apply proper bias voltage to MPPC for some reasons.
reflector still to be optimized
Overall positron time resolution is a little worsened. 33ps -> 37ps (EJ228)

## Slide 18: Summary and Prospects
summary
  Pixelated timing counter with an improved timing resolution is under development for MEG upgrade.
  Basic properties of single pixel were measured with smaller counter.
    Good resolution confirmed
    Bias dependence and effect of temperature variation are studied.
    -> temperature control might be necessary.
    Effect of parallel connection is small.
  Construction and test of single pixel prototype is started.
    Though it have not been optimized yet, reasonable resolution is already achieved.
prospects
  Solve the problem that proper gain cannot be applied.
  Optimize the single pixel performance (reflector, size)
  Optimize the layout
  Construct the prototype detector with several tens of pixels
    Beam test
    Prove multiple hit scheme

## Slide 19: Thank you

## Slide 20: Back up

## Slide 21: Cost
Cost estimate for the new pixelated timing counter

## Slide 22: Time Schedule

## Slide 23: Radial hardness
Results from the irradiation tests of Hamamatsu MPPC (S10362-33-050C) performed by the PSI SR group. Significant increase of dark current (top) and 15% gain degrease (middle) are observed, while the timing resolution is unchanged (bottom).
Courtesy of Dr. A. Stoykov of Paul Scherrer Institut.

## Slide 24: Charge -> Energy
A. Stoykov et al. NDIP 2011
Match the charge peak with energy peak(use μSR group’s result)
→

## Slide 25: I-V curve
↑Parallel connection
single
Break down voltage

## Slide 26: Reference charge dependence

## Slide 27: Single VS parallel(Q/A)

## Slide 28: Electric noise
The one side of counter signal is divided two and connected DRS’s two channels respectively.

## Slide 29: Position reconstruction
BC422
-> attenuation length
-> scintillation light speed
BC422
EJ228
EJ228
↓
Since attenuation length is long, position reconstruction by charge does not work.
Resolution ~14.5 mm
Resolution
~7-9 mm
=> Using time difference is better for position reconstruction.

## Slide 30: Position dependence (lsc)

## Slide 31: Position dependence(μSR)
Slight position dependence in resolution:
~ a few ps
Position dependent time bias: ~40ps

## Slide 32
Properties of ultra-fast plastic scintillators from Saint-Gobain

## Slide 33: New Tracker candidates

## Slide 35: EJ228(100cm)
Notes: プロット->どのくらい？

## Slide 36: BC422(8cm)