## Slide 1: MEG II 実験液体キセノンガンマ線検出器に向けた再構成法の研究 Development of the event reconstruction method for MEG II liquid xenon detector
小川真治、 他MEG IIコラボレーション
@日本物理学会 2015年秋季大会

## Slide 2: Table of contents
1. Introduction of LXe detector in MEG II.
2. Performance of LXe detector
3. Signal readout method comparison
4. Effect from the uncertainty of PDE
5. Summary

## Slide 3: Upgrade of LXe detector for MEG II
Replace PMT of γ-entrance face to MPPC
  Photon collection efficiency becomes uniform
Change PMT alignment of lateral face
  Energy leak decreases
MEG
MEG II
(CG)
MEG
MEG II
wider
log scale
log scale
MEG
MEG II
Imaging
power improves
γ
γ
2 inch PMT
12×12 mm2
MPPC

## Slide 4: 2. Performance of LXe detector

## Slide 5: Performance estimation
Performance improvement of LXe detector has already been confirmed by MC simulation.
  “MEG Upgrade Proposal (arXiv:1301.7225)”
  日本物理学会第70年次大会 21pDK-6
We carried out the performance estimation again.
  Finalized design of the detector
  Improved and optimized analysis
MEG I:red
MEG II:blue
depth < 2cm
40% of events
Eσ
2.4%
↓
1.1%
depth > 2cm
60% of events
Eσ
1.7%
↓
1.0%
Energy Distribution for signal γ
MEG I:red
MEG II:blue
MEG I:red
MEG II:blue
Position resolution vs. depth

## Slide 6: Detection efficiency
Detection efficiency for signal γ-ray in the detector acceptance.
  Defined as the fraction of events whose energy deposit in LXe is over 48MeV
  Design of the material before γ entrance face has been finalized.
Improvement by 9% is observed from MEG I.
  Thanks to the reduced amount of material in the entrance face,
  Consistent with rough estimation in previous study (69%).
 | MEG I | MEG II (this study)
Efficiency | 64.7% | 70.4%
9% improvement
Support structure (CFRP)
spacer (FR4+Cu)
silicon
spacer (FR4)
Assembly PCB (FR4+Cu)
silicon
quartz
ceramic
Filled with LXe
ceramic
7mm
1.4mm
1.6mm
1.4mm
2.5mm
Cryostat wall
MPPC
package
Material before entrance face (not to scale)

## Slide 7: Event reconstruction
Waveform simulation is performed for each MPPC and PMT.
  Based on the measured properties of MPPC, PMT.
  Crosstalk, after pulse, saturation of MPPC are simulated.
  Same noise level with MEG I is assumed.
Timing and # of p.e. of each MPPC, PMT are obtained by analyzing simulated waveform.
Same reconstruction algorithm with MEG I, optimized to MEG II.
  Position is reconstructed from the number of p.e. distribution on the entrance face.
  Energy is reconstructed from the summation of the photon for all channels, taking into account of different coverage for each channel.
  Timing is reconstructed by fitting the time of each channel, considering TOF and timewalk.
waveform
simulation
waveform analysis
Event
Reconstruction
hit of scintillation
photon
1p.e. waveform
simulated
waveform
# of p.e.
timing
MC simulation
Hit position
Energy
Timing
of γ-ray

## Slide 8: Resolution of LXe detector
Estimated resolution for MEG II LXe detector.
Better resolution than previous estimation.
  Thanks to the analysis optimization
Resolution | MEG II (shown in last JPS) | MEG II (this study)
u/v/w (mm) | 2.7/ 2.3/ 3.7 | 2.2/2.0/2.3
Eγ (w<2cm) | 0.62% | 0.65(4)%
Eγ (w>2cm) | 0.53% | 0.49(2)%
tγ (ps) | 71 (preliminary) | 56(1)
u
v
w
γ
u
v
w
t(rec) - t(MC)
Reconstructed Eγ
depth>2cm
depth<2cm
ns
Energy (MeV)
Energy (MeV)

## Slide 9: 3. Signal readout method comparison

## Slide 10: Signal readout method comparison
Series connection of MPPC will be used.
  To avoid the long time constant caused by the large area MPPC.
  Two candidates for signal readout method
    2p2s (2parallel 2series) connection
    4s (4series) connection
Performance of the detector can be affected.
  Different S/N ratio can affect position, energy, and timing resolution
  Different time constant of waveform can affect timing resolution and pileup.
@7V over voltage | 2p2s connection | 4s connection
gain | 1.6×106 | 0.8×106
leading time | 6.5ns | 2ns
trailing time | 49ns | 33ns
4s
connection
2p2s
connection
※Definition of time constant:
[0]*(exp(-t/leading_time) - exp(-t/trainling_time))
12mm
Four independent MPPC chip on one package

## Slide 11: Signal readout method comparison
Two kinds of noise level are assumed.
  MEG I noise level, higher noise level.
Same resolution for position and energy.
Better timing resolution for 4s connection even under higher noise condition.
We decided to use 4s connection.
MEG I noise level (0.3mV) | 4s connection | 2p2s connection
u/v/w (mm) | 2.4/2.2/3.1 | 2.4/2.2/3.1
Eγ (σ of upper Edge) | 0.67(2)% | 0.68(2)%
tγ (ps) | 60(1) | 69(2)
Higher noise level (1.0mV) | 4s connection | 2p2s connection
u/v/w (mm) | 2.4/2.2/3.1 | 2.4/2.2/3.1
Eγ (σ of upper Edge) | 0.74(3)% | 0.79(3)%
tγ (ps) | 70(2) | 75(2)
※These resolutions are estimated before analysis improvement.

## Slide 12: 4. Effect from the uncertainty of PDE

## Slide 13: Uncertainty of PDE
There is the uncertainty of PDE of MPPC.
  Absolute PDE of MPPC is not well-known.
  Broad distribution of PDE is observed in mass test. We may not be able to measure the PDE correctly for each MPPC in the final detector.
  PDE may have an angular dependence which is not consistent with the expectation from the reflection at silicon surface.
Effects of these uncertainty to the detector performance are estimated.
  MC truth of #of p.e. and timing for each MPPC,PMT are used for simplicity.
PDE distribution measured in mass test
PDE vs. incident angle
17-27% @6.5V over voltage
Broad distribution
PDE vs. over voltage
angular
dependence
incident angle (deg)

## Slide 14: Effect of absolute PDE
Absolute PDE can be smaller than our previous assumption.
We checked the degradation of resolution through statistical contribution at smaller PDE.
We observed the degradation of resolution at very small PDE, but effect seems negligible in the range of our measured PDE.
Red:all depth
Green:depth<2cm
Blue:depth>2cm
Energy resolution
Timing resolution
Position resolution
red:u
blue:v
green:w
measured PDE
measured PDE
measured PDE
※Reconstructed from MC truth of # of p.e. and timing.
Resolution from waveform analysis result is 55ps @ PDE 22%.

## Slide 15: Effect of PDE ratio b/w MPPC and PMT
We will use two kinds of sensors, MPPC and PMT.
We have to estimate the ratio between PDE of MPPC and QE of PMT correctly for the energy reconstruction.
  Energy is the summation of the number of the photon, and PDE (QE) is used for converting # of p.e. to # of photons.
  Event by event fluctuation of the ratio of # of p.e. detected in MPPC and PMT can cause the degradation of energy resolution, if our assumption of the PDE ratio is wrong.
Resolution becomes worse if assumed relative PDE ratio is wrong.
We can estimate the true ratio by scanning assumed PDE in the analysis and finding the PDE at which energy resolution becomes best.
true PDE:22%
Red:all depth
Blue:depth>2cm
Green:depth<2cm
Energy resolution by assuming several PDE for MPPC
(Assumed PDE ratio)/ (True PDE ratio)

## Slide 16: Effect of PDE estimation error
Broad distribution of PDE is observed in the mass test of MPPC.
PDE(QE) of each MPPC(PMT) will be estimated by using alpha source in the final detector. Error of PDE(QE) estimation can cause the degradation of resolution.
Effect from this error to the detector resolution is estimated.
  Error of both PMT and MPPC are taken into account.
  Currently observed distribution is the upper limit of the estimation error.
  Events are simulated with PDE variation and reconstructed by assuming constant PDE.
PDE measured in mass test (at small incident angle )
relative
sigma:6.5%
MPPC
PMT
QE measured in MEG I
relative
sigma:16%

## Slide 17: Effect of PDE estimation error
We compared three cases.
  case A: no estimation error for both MPPC and PMT
  case B: no estimation error for MPPC, 16% estimation error for PMT
  case C: 6.5% estimation error for MPPC, 16% estimation error for PMT
Degradation of the resolution is observed for the energy resolution.
Correct estimation of PDE seems important.
Red:all depth
Blue:depth>2cm
Green:depth<2cm
case A
case B
case C
Energy resolution
Resolution | case A | case B | case C
u/v/w (mm) | 2.2/2.0/2.3 | 2.2/2.0/2.3 | 2.6/2.4/2.6
Eγ (σ of upper Edge) | 0.57(1)% | 0.71(2)% | 0.78(2)%
tγ (ps) | 39(1) | 38(1) | 40(1)
※Reconstructed from MC truth of # of p.e. and timing.
Resolution from waveform analysis result is 55ps @ PDE 22%.

## Slide 18: Effect of angular dependence of PDE
Effect of the angular dependence of PDE is estimated.
  Angular dependence observed in the mass test is assumed in the simulation.
  Information of angular dependence is not used in the reconstruction.
Angular dependence changes the p.e. distribution on the inner face, and reconstructed depth is shifted to shallower.
  Shift is 3-20mm depending on the depth
Shift of reconstructed depth vs. depth
reconstructed depth becomes smaller
angular dependence of PDE
PDE
incident angle (deg)
depth(rec) -depth(MC) (2cm<depth<4cm)
cm

## Slide 19: Effect of angular dependence of PDE
Position resolution
  Small degradation for depth
Timing resolution
  Little effect to timing resolution
Energy resolution
  Decrease of the # of p.e. can be recovered by weighting # of p.e. detected on MPPC.
  Same energy resolution can be obtained even with angular dependence.
Resolution | w/o angular dependence | w/ angular dependence
u/v/w (mm) | 2.2/2.0/2.3 | 2.2/2.0/2.7
Eγ (σ of upper Edge) | 0.57(1)% | 0.58(2)%
tγ (ps) | 39(1) | 41(1)
※Reconstructed from MC truth of # of p.e. and timing.
Resolution from waveform analysis result is 55ps @ PDE 22%.
Sum of # of p.e. (all MPPCs)
blue: w/o angular dependence red: w/ angular dependence
25% decrease

## Slide 20: How to deal with uncertainty of PDE
Effect of absolute PDE
  Little effect to performance.
Effect of relative PDE ratio btw/ MPPC and PMT
  Relative PDE ratio is important for energy reconstruction.
  Can be estimated in the calibration run.
Effect of PDE estimation error
  Effect to the energy is not negligible.
  PDE (QE) estimation for each MPPC and PMT is important.
Effect of angular dependence of PDE
  Reconstructed depth is shifted.
  If we can know the angular dependence, this shift can be corrected.
  A new measurement of angular dependence is being planned (see 27aSN-9).
  Method to know the angular dependence in the final detector will be studied.

## Slide 21: Summary
Performance of MEG II LXe detector are estimated with realistic settings together with the several improvement and optimization of analysis.
For signal readout, 4s connection will be used as it has better timing resolution.
Effects from the uncertainty of PDE are estimated. Some of them are not negligible (especially shift of depth by angular dependence).
How to decrease these effects are being studied.
  We are planning another measurement to further investigate the PDE variation and angular dependence.
 | MEG I | MEG II (in last JPS) | MEG II (this study)
efficiency | 64.7% | not estimated | 70.4%
u/v/w (mm) | 5/5/6 | 2.7/2.3/3.7 | 2.2/2.0/2.3
Eγ (depth<2cm) | 2.4% | 0.9% | 0.9%
Eγ (depth>2cm) | 1.7% | 0.9% | 0.8%
tγ (ps) | 67 | 71 (preliminary) | 56
0.7% contribution are assumed for MEG II (from unsolved difference between MC and real detector in MEG I)

## Slide 22: Backup

## Slide 23: abstract
MEG実験のアップグレードであるMEG II実験では!LaTeX$\mu \rightarrow e \gamma$ 崩壊の探索感度を一桁向上させることを目指している。
MEG II実験では約4000個のMPPCを用いた液体キセノンガンマ線検出器を使用する予定であり、位置分解能およびエネルギー分解能の大幅な改善を見込んでいる。
シミュレーションを用いた評価により物理目標達成に必要な分解能がすでに確認されているが、さらなる性能向上を目指して再構成法の改良および信号読み出し手法の最適化を行ってきた。
本講演では開発の現状および結果について報告する。

## Slide 24: Layout of PMT on top/bottom face
We observed that events near top/bottom face show worse energy resolution than other events.
We tried to improve this, by modifying the layout of PMT on top/bottom face.
  Number of PMT increases from 54 to 73 for each face.
  PMT is placed staggered to improve photon collection uniformity.
Improvement of energy resolution near top/bottom can be seen. (though it is not so clear)
black: old layout
red:new layout
Old Layout
New Layout
Energy resolution vs. v
fiducial volume

## Slide 25: Detection Efficiency
67.9
23.9
3
9
15
20.9
59
65
Efficiency(%) | MEG I | MEG II
region 1 | 55.9 | 61.5 ± 1.4
region 2 | 55.0 | 60.3 ± 1.8
region 3 | 61.7 | 70.6 ± 1.2
region 4 | 56.3 | 62.3 ± 1.0
region 5 | 63.8 | 69.0 ± 0.6
region 6 | 66.5 | 71.9 ± 0.6
region 7 | 67.1 | 73.5 ± 0.6
region 8 | 67.9 | 72.9 ± 0.8
Averaged with area | 64.2 | 70.0
Averaged with MEG I weight | 64.7 | 70.4
u(cm)
v(cm)
fiducial volume
fiducial volume

## Slide 26: Setting for MC
PDE | Gain | Crosstalk Prob. | Afterpulse Prob.
22% | 0.8 ×106 | 15% | 15%
0.8M Gain
15%
Crosstalk Prob.
17-27% @6.5V over voltage
PDE vs. over voltage
22% PDE
Event by event fit | 2p2s | 4s
trailing time const. | 49ns | 33ns
leading time const. | 6.5ns | <2ns
4s
2p2s
measured waveform of 1p.e.
measured waveform of 1p.e.

## Slide 27: Waveform analysis
In waveform analysis, charge (# of p.e.) and timing are calculated.
Charge is calculated from fixed integration range.
Constant fraction method is used for timing calculation (with 10% of pulse height threshold)
constant
fraction time
integration range 200ns
pulse height * 0.10
simulated waveform

## Slide 28: Waveform analysis for over range channel
As PDE and gain increases, 35% of event have at least one channel in which pulse height becomes higher than dynamic range of waveform digitizer (950mV).
We can avoid over range by decreasing amp gain but it leads to worse SN ratio, and it may result in worse resolution. (Quantitative estimation has not done yet.)
However, appropriate waveform analysis to these over range channel is important for reconstruction as they have large # of p.e.
Number of over range
channel per event
35% event have over range channel
some channels
become over range
Pulse height vs #ofp.e.
black:MPPC
red:PMT

## Slide 29: Waveform analysis for over range channel
For these over range channel, TOT (Time Over Threshold) method are used for charge calculation in MEG I.
Same method can be used for MEG II.
Relation between TOT and charge are calculated beforehand.
In this study, over range channels are not used for timing calculation.
150mV
TOT
simulated waveform (over range ch)
(#of p.e. from wf analysis)
/(#of p.e. of MC truth)
Red:Over Range channel (Npe>5000)
Blue:Normal channel (Npe~4000)
DRS dynamic
range
0.2% rms
4% rms

## Slide 30: Position reconstruction
Position is reconstructed by fitting # of p.e. distribution of inner face with the solid angle from conversion point to each MPPCs.
Correction of shower direction is applied.
We estimated position resolution by comparing with MC truth.
u
v
w
γ
u
v
w
古い絵差し替え
Notes: \chi ^2 _{pos}=\sum_{i} \frac{N_{pe,i} - c \times \Omega _i (u,v,w)}{\sigma(N_{pe,i})}

## Slide 31: Global Correction
Global correction for U is coming from average shower direction.
Shower direction is not perpendicular to inner face in UR space.
This is not the case for V, as inner face is perpendicular to in VR space.
Global correction for W is basically a offset depending on FitRange.
UR space

## Slide 32: Global Correction
U,W is corrected as a function of U,W
offset
average shower
direction
u(rec)-u(MC)
v(rec)-v(MC)
w(rec)-w(MC)
u(rec)
v(rec)
w(rec)
u(rec)
v(rec)
w(rec)
with FitRange[0]
16 MPPC

## Slide 33: Shower Correction
Correction of event by event fluctuation of shower direction.
If we use wider fit range, the effect from shower direction increases.
Information of shower direction can be derived from difference of the fit result using different fit range.
This correction is applied for UV.
Dependence can be seen also for W, it is also corrected.

## Slide 34: Shower Correction U
U before correction
y axis: u(rec,iRegion) - u(MC)
x axis: u(rec,iRegion+1) - u(rec,iRegion)
iRegion=0
iRegion=1
iRegion=2
iRegion=3
iRegion=4

## Slide 35: W threshold optimization
Wthreshold[6] is decided from resolution for each fitting range.
Resolution of U vs W
Resolution of V vs W
Resolution of W vs W
with Global correction,
and Shower correction
Wthreshold[6]={3,5,9,14,14,40}

## Slide 36: Energy reconstruction
Energy is reconstructed by the summation of the number of photon (not photoelectron) from all channels taking into account of different coverage for each channel.
Correction as a function of position is applied.
# of p.e.
(PMT,MPPC)
× factor (coverage around sensor)
Reconstructed Energy
w/o position correction
× relative weight
between
MPPC & PMT
Reconstructed
Energy
Correction as a function of u,v,w
# of photon
(PMT,MPPC)
×1/PDE
Correction of crosstalk & after pulse
MC truth or
waveform analysis
× Conversion
factor to
energy

## Slide 37: Timing reconstruction
Timing is reconstructed by fitting the time at each sensor, taking into account of TOF from the reconstructed conversion point.
Error of the timing is a function of # of p.e.
Calibrations of timewalk effect and calibration with position are done.
Error of timing as a function #ofp.e.
Error of timing as a function #ofp.e.
MPPC
black: MCtruth
red: waveform analysis
PMT
black: MCtruth
red: waveform analysis
ns
ns
1/sqrt(#ofp.e.)
1/sqrt(#ofp.e.)

## Slide 38: Position resolution
Improvement of position resolution for shallow event from MEG I can be seen as we expected in proposal.
black: MC truth
red: waveform analysis

## Slide 39: Energy resolution vs position
Same resolution for all position with MC truth.
blue:Waveform simulation
red:MCtruth w/o CTAP,saturation

## Slide 40: Timing resolution vs. position
blue:Waveform simulation
red:MCtruth w/o CTAP,saturation

## Slide 41: Comparison with reconstruction from MCtruth
We also tried reconstruction using MCtruth of # of p.e. and timing for each MPPC,PMT for comparison.
  Effect from crosstalk, after pulse, saturation, noise can be seen.
Almost same resolution is obtained for position and energy.
Different timing resolution is observed.
  This can be coming from the error of timing in the waveform analysis.
  There is the room for the improvement in the waveform analysis.
Resolution | MC truth | waveform analysis
u/v/w (mm) | 2.2/2.0/2.3 | 2.3/2.0/2.4
Eγ (w<2cm) | 0.70(4)% | 0.65(4)%
Eγ (w>2cm) | 0.45(2)% | 0.49(2)%
tγ (ps) | 39(1) | 56(1)
Error of timing as a function #ofp.e.
Error of timing as a function #ofp.e.
MPPC
black: MCtruth
red: waveform analysis
PMT
black: MCtruth
red: waveform analysis
1/sqrt(#ofp.e.)
1/sqrt(#ofp.e.)

## Slide 42: Wrong PDE ratio b/w MPPC and PMT
assumed PDE/true PDE=1.1
assumed PDE/true PDE=0.6
assumed PDE/true PDE=2.0
wrong ratio changes reco.E vs. w
This change can be calibrated in the calibration run

## Slide 43: Wrong PDE ratio b/w MPPC and PMT
assumed PDE/true PDE=1.0
assumed PDE/true PDE=0.5
assumed PDE/true PDE=2.0
Event by event fluctuation of detected # of p.e. for MPPC and PMT
causes degradation of resolution with wrong PDE ratio.
x-axis: # of p.e.(MPPC) / # of p.e. (PMT) taking into account different coverage
y-axis: reconstructed Energy
selecting events in abs(u)<5 && abs(v)<15 && 3<w<4

## Slide 44: Reproducibility of PDE fluctuation
Case C(PMT QE distribution 16% + MPPC PDE distribution 6.5%)
Reproducibility of the result is confirmed with different seed value.
Energy resolution
red: all depth
green:depht< 2cm
blue: depth> 2cm

## Slide 45: angular dependence
LXe -> Siへの透過率
blue: s wave
green: p wave
red: average
calculated from complex refractive index
LXe: 1.61
Si: 0.8+2.2i
red: angular dependence measured in mass test
blue: angular dependence measured in mass test (w/o LXe to Si reflection)
incident angle (deg)
incident angle (deg)

## Slide 46: Additional angular dependence meas.
Large chamber
gas Xe
~20 MPPCs
on moving stage
α
α
α
Liquid Xe
Small chamber
MPPC
(4 chips)
We plan to do two different type of tests.
Quick setup, only 4 chips
Confirm angular dependence
Movable stage, 20~30 MPPCs.
Check the angular dependence and MPPC by MPPC variation of PDE
↑ Today’s topic
10cm
70cm

## Slide 47: Energy reconstruction (w/ angular dependence)
Sum of # of p.e. (all MPPCs)
blue: w/o angular dependence red: w/ angular dependence
25% decrease