## Slide 1: MEG II 実験のための 陽電子タイミングカウンターの開発 PSIでのハイレートビーム試験 Development of Positron Timing Counter with SiPM for MEG-II Experiment Beam Test Result in the high rate environment at PSI
西村美紀 （東大）
他 ＭＥＧコラボレーション
日本物理学会 2015年 第７０回年次大会
早稲田大学 早稲田キャンパス

## Slide 2: Contents
Physics Motivation
MEG II Experiment
Positron Timing Counter
Beam Test ＠PSI (←MEG II Site)
Status & Schedule

## Slide 3: Physics Motivation
Search for cLFV (charged lepton flavor violation), μ+ e+γ decay
  Forbidden in the SM
  Sizable branching ratio is expected by many bSMs
Most stringent upper limit of the branching ration is set by the MEG experiment;
90% C.L. (Phys. Rev. Lett. 110(2013) 201801)
Already started exploring bSM region!
Upgrade MEG experiment (MEG II)
An example, the expectation of the BR from SU(5) SUSY-GUT
M. Cannoni et.al., Phys. Rev. D 88, 075005 (2013)
Mass of right handed neutrino

## Slide 4: What should we measure?
We should measure
Timing・Position・Momentum precisely.
Accidental BG
Dominant
Physics BG
Signal
Background

## Slide 5: MEG II
Xenon Calorimeter
SiPM readout
Pixelated Positron Timing Counter (TC)
Radiative Decay Counter
Stereo wire drift chamber
Tracking the positron till near TC
e
γ
µ
twice higher beam intensity
（stopping µ ~7×107）
sensitivity
中浦 24aDL11
澤田・家城・小川
(21pDK4,5,6)
This talk, and next talk 吉田
(24aDL10)

## Slide 6: Pixelated Positron Timing Counter
~9
target
~9
× 512
4 cm or 5 cm
12 cm

## Slide 7: Pixelated Positron Timing Counter
4 cm or 5 cm
12 cm
Thickness 5 mm
6 SiPMs in series at the both end
AdvanSiD (Italy) 3x3 mm2, 50 um
Fast Plastic Scintillator
BC422, rise time 0.35 ns
attenuation length 8 cm
PCB
Cable（RG178）
Non-magnetic
PCB
Back plane
Long PCB ~80 cm
Multi layer, coaxial like

## Slide 8: Principle
Many hits
  Averaging timing information, final TC resolution improve.（We already prove the principle in the other beam tests.）
Pile Up Reduction
  Beam intensity becomes higher in MEG II
Able to track the positron
Resolution vs. # of hit counters
Number of hit counters (MC)
MEG I: 80 cm scintillator bar （with 2 PMTs） ×15
MEG II: 12 cm scintillator counter ×250
σsingle = 65 ps
*contribution from DC; 75 ps
σsingle = 65 ps *contribution from DC; 11 ps
σ ~30 ps
~5 ps
~30 ps

## Slide 9: Status
Prototype test
  Good single counter performance was already demonstrated.
  Multiple hit scheme was proved by beam tests in a quiet environment.
    Positron beam at BTF in Italy
    50 Hz, 1-2 positrons in a bunch
Calibration (next talk)
  Laser
  Michel positron
Software development
  Timing reconstruction method

## Slide 10: Beam test

## Slide 11: Motivation
Previous beam test was conducted at low positron rate. (~50 Hz)
However in MEG II , TC will suffer high rate positron backgrounds (>~45MeV, <~180kHz)
Operate TC in this high rate environment.
Length [cm] | Average Rate (kHz) | Highest Rate (kHz)
12 | 70.2 | 174
From MC study (height is 4 cm)
muon normal decay

## Slide 12: Set up
Back plane
We had to use scintillators and SiPMs of bad performance due to quality control issues of vendors.
Muon Beam
πE5 beam line at PSI
~108 Hz DC beam
2 small counters
5x5x5 mm3, 1 MPPC
Teflon wrapping
Time Reference
Michel Positron
Normal decay from stopping muon
The same as real background
We can get time uniform background.
8 Prototype Counters
6 for 120x40x5 mm3, 2 for 120x50x5 mm3
AdvanSiD w/o new technology -> w/ new technology
Scintillator BC422 -> EJ232
Reflector 3M Mylar film, light shielded
Collimator
Digitizer (DRS)
1.6 GHz
Coincident Trigger

## Slide 13
Prototype Counters
Reference
Counters
Positrons
Back Plane
Counter A
Counter B
Counter C
…

## Slide 14: Rate
Chart: Counters
| BTC21 | BTC22 | BTC23 | BTC24 | BTC25 | BTC26 | BTC27 | BTC28
Michel low | 64 | 55.5 | 46.8 | 37 | 30 | 24.2 | 21.7 | 17.8
Michel expected | 166 | 147 | 123 | 100 | 83 | 69 | 69 | 53
Michel high | 290 | 258 | 210 | 168 | 136 | 116 | 113 | 89
We adjusted the beam slit for rate scanning (3 points)
Three hit rate conditions
Low rate; 17.8 – 64 kHz
Expected rate; 53 – 166 kHz
High rate; 89 – 290 kHz
5 cm height
Expected rate in MC
Length [cm] | Average Rate (kHz) | Highest Rate (kHz)
12 | 70.2 | 174
From MC study (height is 4 cm)
B
C
D
E
F
G
H
A

## Slide 15: Analysis
Single Counter
Timing
Position
Clustering
  Clustering based on reconstructed time.
  Cut the pile up hits
Tracking
  Using reconstructed position
  Far hits from trajectory are removed.
Notice: There is trade-off b/w strict cut and efficiency.
We should optimize the parameter for final analysis

## Slide 16: Single Counter Resolution
Small degradation of the resolutions from higher rate can be observed.
Back plane seems to pick up noise
A
B
C
D
E
F
G
H

## Slide 17: Overall Resolution
Only small degradation of the resolution up to the expected hit rate.
N = 2
N = 3
N = 4
N = 5
N = 6
N = 8
N = 7
(*Average)

## Slide 18: Overall Resolution
The difference becomes larger in higher rate. However the difference is not so effective especially b/ lower rate and expected rate.
At n = 8, the overall resolution is ~35 ps.
  This number will improve with final counters because the single resolutions will improve from ~90 ps to ~65 ps.

## Slide 19: Schedule & Status
In this beam test, we demonstrated good performance in high rate environment expected in the experiment.
It is time to construct and test the final detector.
Construction
  SiPMs were already delivered and tested.
  Support structure is under construction.
  SiPMs array will be tested soon.
  Counter mass production and mass test
TC DS engineering run is planned in Dec.
  Down stream of TC will be installed and tested with the muon beam.
  Number of readout electronics channels are limited. (Half of the DS TC channels can be readout at one time)
Next spring TC US will be installed.
Summer in 2016, the engineering run will start.
Following the engineering run, physics run will start.

## Slide 20: Summary
The MEG II experiment will search for μ→eγ decay at a unprecedented sensitivity of 4x10-14.
The Pixelated Positron Timing Counter of 30 ps resolution is in preparation.
We conducted a beam test with prototype counters under the MEG II beam condition.
  We obtained the excellent resolution of 35 ps with 8 counters.
  The final performance of TC will be better by using better counters.
Preparation for TC DS engineering run in Dec. is underway.

## Slide 21: Back up

## Slide 22: Pileup Study
Michel positron (4π, all momentum)
Hit rate of Michel positron depends on position.
The bins correspond to the each pixel.
90x30x5 pixels
The highest rate position

## Slide 23: Final Performance
We could measure the final prototype counters. (only two counters)
The TC performance improved.
In the final detector better performance is expected.

## Slide 24: Time line
Beam
  We lost ~6 days for the investigation.
Sun | Mon | Tue | Wed | Thu | Fri | Sat
12 | 13 | 14 | 15 | 16 | 17 | 18
19 | 20 | 21 | 22 | 23 | 24 | 25
26 | 27 | 28 | 29 | 30 | 31 | 1
2 | 3 | 4 | 5 | 6 | 7 | 8
9 | 10 | 11 | 12 | 13 | 14 | 15
16 | 17 | 18 | 19 | 20 | 21 | 22
TC set up
Beam investigation
Beam tuning
Beam
investigation
Beam investigation
Michel
Data taking
WD test
Beam tuning for Positron
Mott
Beam shat down
Michel
Beam tuning
TC set up delivered
TC alignment
ATAR beam time