## Slide 1: Engineering run of the MEG II downstream Radiative Decay Counter in the muon beam
家城 佳,
他MEG IIコラボレーション
II

## Slide 2
MEG II
RDC detector
Engineering run

## Slide 3
MEG II
RDC detector
Engineering run

## Slide 4: μ  eγ search
MEG
is the good probe for new physics.
MEG II will search for with 10 times better sensitivity!
e+
γ
μ+
μ+
e+
γ
BSM
(ex. SUSY)
MEG II

## Slide 5: MEG II experiment
Additional detector to identify BG events家城、岩井
21aSE-6,7
intensity 2 7107 μ/s
LXe γ detector
小川, 松澤
22aSF-9,10
e+ drift chamber
& timing counter
西村、中尾、宇佐見
23aSG-3,4、23aSF-9
γ
e+
2
all resolutions
e+ efficiency
2
Detectors will be ready by 2017!
μ+ beam
Summary talk
内山 21aSE-1
gradient
B-field

## Slide 6
MEG II実験
RDC detector
Engineering run

## Slide 7: Radiative Muon Decay
Radiative Muon Decay Annihilation In Flight (RMD, ) (AIF, e+e-  2γ)
γ
μ+
e+
μ+
e+
γ
+
signal
Main BG (accidental)
2 : 1
Sources of BG γ (Eγ > 48MeV)
Ee=Eγ=52.8 MeV
Back to back
Time coincidence
RDC aims to identify RMD

## Slide 8: Radiative Decay Counter (RDC)
LXe detector
μ beam
e+ drift chamber
e+ timing counter
RMD γ
RMD e+
accidental e+
US RDC
DS RDC
RMD events can be identified by detecting low energy e+ which is coincident in time with γ detected by LXe.
※not
approved yet
 next talk
RDC may reduce the γ BG to half and improve the μeγ sensitivity by 23%.
 this talk

## Slide 9: DS RDC (Plastic Scintillator)
LXe-PS timing diff (MC)
19cm
2 or 3 MPPCs (S13360-3050PE) at both ends,
connected in series
12 counters with
reflector & light shielding
Accidental e+
RMD + AIF (γ at LXe)
Plastic Scintillator (PS) detects the timing of e+.
RMD peak

## Slide 10: DS RDC (LYSO crystal)
LYSO distinguishes RMD e+ and Michel e+ by energy.
MPPCs (S12572-025P) are pushed with spring
2cm cube crystal 76
Energy distribution (MC)
RMD e+ (Eγ>48MeV)
Michel e+

## Slide 11
MEG II
RDC detector
Engineering run
Setup & calibration
Analysis of RMD event

## Slide 12: Engineering run
e+
γ
μ+
BGO
RDC
Purposes:
- RMD detection capability test
- Identify problems
Operation test of complete detector in the μ beam for the first time
Date:
30 Jun. ~ 8 Jul. 2016
BGO crystals were used as γ detector instead of LXe detector.
4.6cm
20cm
BGO detector

## Slide 13: Mounting & signal check
Moving arm RDC is mounted on moving arm which allows the LXe calibration target etc. to be inserted from DS.
Feed-through A PCB-based feed-through transmits the signal from vacuum to outside.
Signal check Unfortunately, we found 4 bad channels in PS out of 24. The conductive epoxy that connects MPPCs on board was mechanically weak.  To be repaired
feed-through
movable
RDC

## Slide 14: Electronics: WaveDream
WD readout vs. pulse gen. input
Board 2
Board 3
Board 4
Board 5
Board 6
Board 7
We used this board for all detectors.
WaveDream: Waveform digitizer + Amp. & shaper + HV Being developed @PSI for MEG II
Non-linearity was found in the waveform input/output. We correct this effect by using a response function obtained by using pulse gen.
Current of the LYSO channels were above the maximum rate (~500A) for the central part of crystals, so we had to lower the HV.
 We can fix these issues in the next time.

## Slide 15: Waveform analysis
Example of PS waveform
Example of LYSO waveform
PS hit was reconstructed by requiring a coincidence of both side of MPPCs.
LYSO energy is calculated for each pulse by integrating the waveform.
Gain 100, shaper on
Gain 1, shaper off

## Slide 16: Calibration of LYSO
We calibrate LYSO crystals using intrinsic radiation signal.
Fit function is:
Energy
88
202 +88
307 +88
307+202 +88
(γ peaks + β decay spectrum) ⊗ Gaussian smearing (σ = Eres)
Example of the fit

## Slide 17: Calibration of BGO detector
88Y charge
γ 0.898MeV
γ 1.836MeV
Cosmic-ray energy
The absolute energy of BGO crystal is calibrated by using 88Y source.
Channel-by-channel relative calibration is done by using cosmic-ray.
Energy scale problem:
The energy deposit of cosmic-ray is ~20% lower than expected.

## Slide 18: Physics data taking
We took data with MEG II μ beam intensity.
Trigger: Any hit in BGO, ~70k events
BGO energy spectrum
Trigger threshold for BGO was ~ 35 MeV, if the calibration with 88Y is correct.
(It was thought to be ~44 MeV assuming that the CR energy is correct.)

## Slide 19
MEG II
RDC detector
Engineering run
Setup & calibration
Analysis of RMD events

## Slide 20: Example of events
Example of CR candidate
Example of RMD candidate
marker size ∝ energy
color ∝ time
Cosmic-ray events needs to be removed in event selection.

## Slide 21: RMD event selection
We require that the largest hit in BGO to be found in the central four crystals.
2. Then, the energy sum in BGO must be below 55 MeV.
select
Example of RMD candidate event
Beam on data
Beam off data
(CR only)
BGO energy sum
 98% of CR events are removed
fiducial volume

## Slide 22: PS-BGO time coincidence
PS-BGO timing difference
RMD peak
flat region: Accidental Michel e+
A clear peak that correspond to RMD events is observed.
BGO energy scale problem needs to be understood for the quantitative comparison of data and MC.
Preliminary

## Slide 23: LYSO energy cut
PS-BGO timing diff
w/o LYSO cut
w/ LYSO cut
LYSO sum energy
select
(CR veto is applied)
RMD e+?
Michel e+?
As expected, accidental BG reduces by applying a cut in LYSO energy.
RMD events also reduced too much with this cut, which is probably because the BGO energy threshold is too low and the energy of RMD e+ is high.
Preliminary
1/10
1/2
LYSO sum energy = sum of hits in coincidence with BGO

## Slide 24: Summary
MEG II RDC detector is constructed and tested with the μ beam for the first time.
Operation of the RDC detector was in general successful.
Preliminary result of the analysis is shown. RMD events were clearly seen in the PS-BGO timing difference plot.
Analysis is ongoing to compare the performance of the detector with simulation.

## Slide 25: Backup slides

## Slide 26: Non-linearity
The linearity of the response was found to be bad.
Ryoto measured pulse height of the pulse generator signal as a function of input pulse height.
WD readout vs. pulse gen. input
Board 2
Board 3
Board 4
Board 5
Board 6
Board 7
Example of averaged waveforms
(input: function generator)
Input height [mV] = 100, 1000, 2000
Scale = 1, 1/10, 1/20
Correction is applied for each bin in the waveform, using the input/output response measured with function gen.
Correction seems to be good.
before correction
after correction

## Slide 27: Calibration: to do
PS energy calibration (using Michel e+) is not done.
Temperature correction is not implemented.
RDC temperature history
sensor 0 (inside light shielding)
sensor 1 (outside light shielding)
(Temperature inside the light shielding seems to become high when the beam is on.)

## Slide 28: LYSO current history

## Slide 29: Calibration: LYSO intrinsic
(Shota’s
MSC thesis)
Example of charge distribution
Fitting function is provided by Ryu. It is a convolution of:
(gamma peaks + beta decay spectrum) ⊗ gaussian smearing (σ = Eres)
In the data, we found a sharp peak below the main peak, which does not agree with fit function. It seems to be caused by intrinsic radiation γ escaped from the crystals in the neighbor. We remove those events by requiring Nhit=1 in event.

## Slide 30: Beam data: raw energy distributions
BGO energy sum
LYSO hit energy
We took data assuming that the threshold is around 44 MeV, but in fact the threshold is around 35 MeV.
This might be wrong by ~20%.

## Slide 31: PS hit & clustering
Time difference of plate hits
“Hit”
  Pulse from two sides of the plate are combined to a single hit, when the time difference is less than 5ns.
“Cluster”
  Hits with time difference < 5ns are clustered.
Time difference hits from two sides of the same plate

## Slide 32: Number of RMD events
NRMD = (Nevents in ±15ns region) – NBG = 2367.6
from the fit in the flat region
NRMD_expected = Ntrig * (US/DS ratio) * (acceptance) * (fraction of working ch) * (RMD/(RMD+AIF))
0.48
0.88 when Eγ>48MeV
90.6%
We compared the number of RMD events with expectation in the following way.
dead ch
Plate hit distribution
In order to do the comparison correctly, BGO energy calibration problem needs to be understood.
Eγ>48MeV is assumed for the expectation, but this cut is not applied in this analysis.
Acceptance and RMD/(RMD+AIF) are overestimated.
0.65
15447 after CR veto
= 3869.2
CR veto is applied.
|Tdiff|<5ns is required.

## Slide 33: LYSO energy vs. PS-BGO timing

## Slide 34: Event reduction by LYSO cut
After / before cut