## Slide 1: 大強度粒子ビーム中で動作する MEG II実験 輻射崩壊同定用カウンターの開発
家城 佳、岩井 遼斗
他 MEG II コラボレーション

## Slide 2: search
e+
γ
μ+
μ+
e+
γ
BSM physics (e.g. SUSY)
is lepton flavor violating decay
Observation = Evidence of BSM physics
Current limit: 4.2x10-13 (90%C.L., ) by MEG
BSM prediction: O(10-14) (e.g. SUSY-seesaw)
MEG II goal:
4x10-14

## Slide 3: MEG II @ PSI
μ+
γ
e+
MEG
MEG II
Upgrade
- x2 beam rate
- x2 resolution
- x2 efficiency
x10 better sensitivity
Detector upgrade is completed except for e+ drift chamber!
LXe detector
e+ drift chamber + timing counter
Radiative Decay Counter

## Slide 4: Radiative Decay Counter (RDC)
γ
e+
μ+
Chart: 
 | 0.65421
 | 0.34579
Source of BG γ
RDC detects these BG!
RMD
AIF
(e+ Annihilation In Flight)
0
20
40
60
80
100%
(Eγ>48MeV)
RDC identifies Radiative Decay
main source of BG
…by detecting time coincident low momentum
DS
RDC
US
RDC
DS
US

## Slide 5: Downstream detector
Plastic Scintillators (PS)
Measure e+ timing
 will have e+ & time coincidence
12 fast plastic scintillators (BC418) + 2~3 MPPCs connected in series at both ends
20cm
LYSO crystals
Measure e+ energy
 will have small energy (1~2MeV) compared to BG ()
76 LYSO crystals (2x2x2 cm3) + MPPC
Construction is finished.
Performance was tested in beam.
(JPS2016Autumn 21aSE06)

## Slide 6: Re-production & test
Soldering
Conductive epoxy (different SiPM)
Light yield with PS
PCB
SiPM
Bad channels were found in the performance test.
Electric connection on plastic scintillator was unstable.
We used conductive epoxy instead of soldering to avoid heat damage  fragile
All counters are reproduced by soldering.
Light yield did not change.
Resolution was measured to be good
for all ch (90~100ps, 90Sr source)

## Slide 7: Installation
μ
e+
RDC
feed-through
pneumatic pump mover
allows insertion of calibration target from DS
DS RDC is installed!
To be tested in beam with LXe detector in the end of this year.

## Slide 8: Upstream detector
Upstream detector is must be placed in the beam before stopping target.
● Requirements
- Thin (not to affect the beam optics)
- Operational in high rate (~108/s)
JPS2017Spring, 18aK33-6
● Possible candidate 250 m scintillation fiber + SiPM readout
Thin, fast response  operational in high rate beam
However, radiation damage might be serious.
<1/2 light yield decrease expected in 2 weeks.

## Slide 9: Diamond sensor
Diamond is an other candidate for US RDC.
☺ Radiation hard
☺ Can be very thin (~100m)
☺ Fast (<1ns)
😐 Small signal
It works similar to Si detector
e+ energy deposit is only ~50 keV for100m diamond.
Energy to create an e/h pair = 13eV (c.f. It is only 3.6eV for silicon.)
Properties:

## Slide 10: Synthetic diamonds
Test of diamond samples: 4mm x 4mm x 100m, Applied Diamond, Inc.
4 mm
CVD (Chemical Vapor Deposition) diamonds are commonly used for sensors.
Two types of crystals are available:
Single crystal (scCVD): large signal, expensive Polycrystalline (pCVD): small signal due to trapping on boundaries, but cheap
polycrystalline diamond
Au (200nm) on both sides as electrodes

## Slide 11: Test of diamond sensor samples
diamond
trigger scintillator
We tested diamond samples with radioactive sources placed on top of it.
Readout:
Charge amp.
Charge amp (CIVIDEC C6HV0177), 5.7 mV/fC,
+ Waveform digitizer
electrodes

## Slide 12: source signal
First, we checked the signal with 241Am alpha source on wire.
α does not reach the trigger scintillator and stops inside diamond.
(Energy deposit ~ 5MeV)
diamond
241Am on wire
Successfully observed the signal!
However, the signal was not observed for the pCVD sample (too small?).

## Slide 13: Pulse height vs.
Pulse height of signal is measured by changing from -50V to +50V
This is because the Charge Collection Distance (CCD) (= Average distance of e-h movement)
reached the size of the diamond thickness.
CCD increases are increase.
Pulse height became maximum around ±20 V.

## Slide 14: source signal
trigger scintillator
diamond
+50V
0V
-50V
Averaged waveform
source signal is small. Energy deposit ~ 50keV.
The signal size (~2mV) was compatible with noise.
Therefore, it was not possible to distinguish the signal from noise.
5mV
The signal can be seen in the averaged waveform.

## Slide 15: Next step
Possible approaches
- Amplifier modification (noise reduction?)
- Use silicon detector
Example:
50m thick silicon detector in Mu3e experiment @ PSI
If upstream RDC can detect radiative decay BG with 100% efficiency, sensitivity will be improved from 4.310-14 to 3.910-14.
Thin, fast, works in high rate
Availability? Radiation hardness?

## Slide 16: Summary
MEG II RDC detector identifies the main BG,
Downstream RDC is already constructed and installed. It will be tested with LXe detector in beam in the end of this year.
Diamond sensor was tested as a candidate for upstream RDC detector. Signal size was measured to be small for the electrons. Other possible solution: silicon detector?