## Slide 1: MEG II実験における 陽電子再構成アルゴリズムの開発 Development of positron reconstruction algorithm in MEG II experiment
西村美紀（東大）
他 MEGIIコラボレーション
日本物理学会 第72回年次大会
大阪大学（豊中キャンパス）

## Slide 2: Content
Introduction of the MEG II Experiment
Positron Spectrometer
Positron Time Reconstruction
TC Tracking
Prospect and Summary

## Slide 3: MEG II Motivation
In MEG II experiment we aim to search for charged lepton flavor violation (cLFV), μ+ e+γ decay.
The SM strongly suppress cLFV .
However sizable branching ratio is expected by many bSMs.
Most stringent upper limit of the branching ratio is given by the MEG experiment.
90% C.L.
(Eur. Phys. J. C 76 (2016) no.8, 434)
Target sensitivity of MEG II is
Simplest Little Higgs Model (arXiv:1610.01266v2)
MEG
MEGII

## Slide 4: MEG II Requirement
Signal: two-body decay
Dominant BG: accidental
<52.8 MeV
Any angle
Time Random
52.8 MeV
Opening Angle 180°
Time Coincident
105.6 MeV
Precise measurement of emission angle, energy, and timing of both positron and γ is essential.
⇒ Today’s topic is performance of positrons time reconstruction.

## Slide 5: Detector
Wire Drift Chamber
Pixelated Positron Timing Counter
Liquid Xenon Gamma-ray Detector
Superconducting Magnet
Muon
Positron
Gamma-ray
Radiative Decay Counter

## Slide 6: Positron Spectrometer
Wire Drift Chamber
Pixelated Positron Timing Counter
Liquid Xenon Gamma-ray Detector
Superconducting Magnet
Muon
Positron
Gamma-ray
Radiative Decay Counter
Positron 1st turn
Positron 2nd turn

## Slide 7: Positron Measurement
Wire Drift Chamber (DCH)
Single volume, low-Z gas mixture (He:iC4H10 = 85:15)
1200 sense wires (2 m long, 20 μm diameter)
Stereo angle (7°) configuration
Pixelated Positron Timing Counter (TC)
512 fast plastic scintillator counters (120x40/50x5 mm3)
6 SiPMs (AdvanSiD) are attached on both side of the counters.
Reconstruct positrons in each detector, then check matching
256 counters for down stream
DCH reconstructs
Momentum and vertex
Track length from vertex to TC
TC reconstructs
Positron passing time through each counter
Single counter

## Slide 8: Performance Study with MC
Check the performance of positron spectrometer in detail with full analysis chain of the positron reconstruction.
Set up
  Geant4
  Signal positron mixed Michel positron @ 7 x 107
  TC: Hit smeared by their resolutions
  DCH: waveform simulation
  In this talk we’ll focus on timing reconstruction.
(TC Waveform simulation study
Usami’s talk 20aA12-1)

## Slide 9: Positron Timing Reconstruction
An example with signal event (w/o pile up)
DCH reconstructs track from vertex to TC first hit. (LDCH)
TC reconstructs time at first hit by each counter.
Measured time by ith counter
Path length from a first counter to ith counter
X-Y
DCH
region
TC
region
― MC track
― propagated track
… DCH Reconstructed hits
TC first hit

## Slide 10: Positron Timing Reconstruction
An example with signal event (w/o pile up)
Z-Phi
(w/ TC)
T1
T2
Ti
― propagated track
★ TC first hit
TC hit counter
DCH reconstructs track from vertex to TC first hit. (LDCH)
TC reconstructs time at first hit by each counter.
Measured time by ith counter
Path length from a first counter to ith counter

## Slide 11: Time Resolution from Each Detector
Resolution coming from Track reconstruction is 14.8 ps.
(75 ps in MEG)
σTC 31.0 ps
2. Time Resolutions in TC
1. Flight Time b/w Target and TC
TC resolution is 31.0 ps.
(76 ps in MEG)
σL 14.8 ps
(sec)
@ first counter (sec)

## Slide 12: Overall Positron Time Resolution
σ = 39.5 ps
Overall positron time resolution is 40 ps.
(It was 108 ps in the MEG experiment.)

## Slide 13: More Development

## Slide 14: Effect of Multiple Scattering in TC
σTC 27.0 ps
σTC 31.0 ps
The effect of multiple scattering in TC is not so large, but if we’ll estimate them more accurate the time resolution should be better.
TC
Track reconstructed by DCH
True Track
TC

## Slide 15: TC Tracking
Motivation is more precise estimation of path length in TC.
TC reconstructs hit position along length.
GENFIT: DAF(Deterministic Annealing Filter) is used.
  It is almost Kalman Filter but with reweighted measurements against outlier hypothesis.
Initial information is a track reconstructed by DCH.
t2
t1
T1
T2
Ti

## Slide 16: Hit Position Resolution
TC tracking recovers the effects of multiple scattering.

## Slide 17: Time of Flight in TC
However reconstructed path length does not change so much.
GENFIT does not have time fit.
More development is need.
rec - MC (sec)
MC (sec)

## Slide 18: Impact on Time Resolution
In this time, time resolution does not improve so much,
because calculation of path length does not improve.

## Slide 19: Summary
The MEG II experiment aim to search for μ+ e+γ decay.
Positrons are reconstructed by DCH and TC.
Full chain of positron reconstruction algorithm is prepared and estimate overall performance.
  Overall positron time resolution is improved to 40 ps from 108 ps in MEG.
There is room for improvement and it’s ongoing.

## Slide 20: Back Up

## Slide 21: Mix overall resolutions

## Slide 22: Positron Detection Efficiency
  Overall Efficiency: 71.1 %
    DCH Efficiency: 81.0 %
      Propagation miss to TC (Dominant ~50 %)
      Contamination
      Vertex reconstruction miss
    TC Efficiency: 90.6 %
      No Hit (9.2 %)
      Clustering contamination > 40% in a cluster (the rest)
    Matching Inefficiency (if both reconstruction is succeeded): 7.6 %
      in the same turn (20.9 %)
      Turn difference is just 1. (58.1 %)
6 % in matching inefficiency
Preliminary

## Slide 23: Positron Reconstruction Chain
TC
Hit Rec.
Clustering
WF analysis
DCH
WF analysis
Hit Rec.
Track finder
Kalman Fit
Matching
Propagation to TC
b/w TC cluster and DCH track
Counters
* Hits
cluster
DCH is tracking just before TC.
Previous JPS
TC is pixelated by 512 scintillator counters.
Positron comes to the TC in high rate. (a few MHz in the TC region.)
→ Clustering of TC hits was developed.

## Slide 24: Positron Reconstruction Chain
TC
Hit Rec.
Clustering
WF analysis
DCH
WF analysis
Hit Rec.
Track finder
Kalman Fit
Matching
Propagation to TC
b/w TC cluster and DCH track
Propagated
Track from DCH
Reconstructed position in TC
Check this difference

## Slide 25
w/o Michel e+
w/ Michel e+
Time Resolutions in TC
Time of Flight b/w Target and TC
Tails are almost the same. These tails come from signal itself.
Multi turn or delta ray may be the reason.
w/o Michel e+
w/ Michel e+

## Slide 26: Tail events from multi turn
Tail in events come from hits from different turns of the same positron.
  They affect final time measurement.
These kind of hits should be separated by
  Tracking
  More precise cut in clustering
2nd turn
1st turn
2nd turn
1st turn
⇒ make positive tail.
⇒ make negative tail.
<

## Slide 27: Time Resolution from Each Detector
Mean 4.5 psec
Sigma 31.0 psec
Time Resolutions in TC
Time of Flight b/w Target and TC
Mean 8.3 psec
Sigma 14.8 psec
Since these two reconstructions does not have correlation, .

## Slide 28: Hit Position Reconstruction
R
cm
cm
R
Reconstructed position – mc position
Counter local
Std Dev 1.5
→ 0.6

## Slide 29: Hit Position Reconstruction
R
Z
φ
L
cm
cm
rad
cm

## Slide 30: Prospects
Weighted hit time by reconstructed hit position
  Closer channel should have larger light amount than the other channel have.
Contamination cut
t2
t1