## Slide 1: MEG II実験：2021年エンジニアリングランの現状と計画 T The MEG II experiment: status and plan of the 2021 engineering run
内山 雄祐 on behalf of MEG II collaboration
日本物理学会2021年年次大会 令和3年9月17日
17pT1-4

## Slide 2: MEG II in search of μ+ → e+γ
Search for μ+ → e+γ down to
6×10-14 (90% C.L. sensitivity)
B(μ+ → e+γ) < 4.2×10-13 @90% C.L.
(while 5.3×10-13 expected)
×2 intensity muon beam
×2 resolution everywhere
×2 efficiency
An intensity frontier experiment
Upgraded from MEG experiment
To get definitive evidence for BSM
MEG result (2016)
UTokyo
KEK
Kobe Uni.
INFN Genoa
INFN Lecce
INFN Pavia
INFN Pisa
INFN Roma
PSI ETHZ
BINP
JINR
UC Irvine
~60 physicists

## Slide 3
LFV
Lepton flavor violation
Low scale
Flavor violation from neutrino Yukawa
B(μ→eγ) ~ 10-11 – 10-14
Flavor violation from quark Yukawa
GUT
Seesaw
SUSY
Ultra-high scale
TeV scale
Force unification Matter unification
Charge quantization
Neutrino mass
Leptogenesis
Spacetime–internal sym. unification
Dark matter?
Solution for hierarchy problem?
top-down

## Slide 4: Other reasons
(g – 2)μ
LHCb
CMS
mu2e/COMET
bottom-up
Limit on μ→eγ provides the most stringent limit on the LFV Higgs decay
BR(h→μe) < 10-8
(CMS limit: BR(h→μe) < 3.5×10-4)
~
Phys. Lett. B 763 (2016) 472, JHEP 03 (2013) 026
Phys. Rev. D 97 (2018) 015019
Strong correlation b/w observed anomalies.
If new particle couples to electron, it induces sizable μ→eγ.
two-loop
tree
μ→eγ

## Slide 5: MEG II
Liquid xenon photon detector (εγ~70%, σE/E~1%)
Pixelated timing counter
(σt ≃ 35 ps)
Cylindrical drift chamber (~1.6×10-3 X0, σp~100 keV)
Thin-wall SC solenoid
(gradient B-filed: 1.3→0.5 T)
Radiative decay counter (identify high-energy BG γ events)
Muon stopping target
(170 μm-thick scintillating film)
μ+
γ
e+
EPJ-C 78 (2018) 380
Continuous μ+ beam (7×107 s-1)

## Slide 6: Current status & outstanding issues
To be studied
Electronics
  Full electronics has not yet been tested.
LXe detector
  Lack of study with full channel readout.
  Degradation of MPPC PDE.
  Evaluation of timing resolution.
Drift chamber
  Stable operation of the detector in beam.
  Bad S/N.
  Lack of tracking study due to limited electronics.
All the apparatus has been constructed.
Each detector has been tested in beam so far.
1
2
3

## Slide 7: Goal of 2021
To address all the issues.
To setup μ→eγ trigger and collect the initial data of MEG II.
1
2
3
To be studied
Electronics
  Full electronics has not yet been tested.
LXe detector
  Lack of study with full channel readout.
  Degradation of MPPC PDE.
  Evaluation of timing resolution.
Drift chamber
  Stable operation of the detector in beam.
  Bad S/N.
  Lack of tracking study due to limited electronics.
Complete production & deploy
Long-term study in beam.
New measurement with improved setup.
Long-term study in beam.
Noise investigation under final condition.

## Slide 8: Electronics
Mass-production finished & installed in Mar.
DAQ with the full channels in operation
  Basically, the system works (debugging ongoing).
  Stable DAQ at data rate of 1.5 Gbps. ~2 TB/day in storage.
Better noise situation for LXe, but worse for pTC.
33 crates, 8500 channels
1

## Slide 9: LXe detector
15pT3-6 小林
  4092 MPPCs + 668 PMTs
Not a simulation!
Commissioning with the full electronics done.
Calibration & monitoring continued.
Using beam from mid. Aug (~1 month)
  To study the MPPC PDE decrease.
  Basically, confirmed previous observations (preliminary). → No sign of saturation of the degradation.
Bad channels:
MPPC 28 ch
PMT 27 ch
Preliminary
LXe detector
2

## Slide 10
High granularity readout
  4092 MPPCs + 668 PMTs
Waveform data for the 4760 channels
  1024 points @ 1.4 GSPS
Pileup identification & unfolding
44 ch
93 ch
See 15pT3-7 恩田

## Slide 11: Drift chamber
Conditioning done
  In beam with high concentration of O2 (2%).
  High current (corona discharge) is reducing.
  Gas mixture: He:iC4H10(90:10) + 1.2% 2-propanol + 0.5% O2
Noise study
  Identified several sources of noise.
  Some were fixed, others require hardware modification.
Tracking study started
  Cosmic ray and e+ from muon decay.
  Calibration and alignment are underway.
58 bad cells (/1280 cells)
7 missing anodes
13 short
HV cable disconnected
3

## Slide 12: Conditioning in beam
MEG meetin - 01/09/2021
Stable at 2% reduce O2: 21.5%
Instabilities at 1.5%
Repeat conditioning
Current (μA)
O2 (%)
1 day

## Slide 13: Building new drift chamber
Risk of wire breaking
  Exposure to humidity during the construction
  Bad coating (Ag) due to an ultra-finishing process to make 40-μm wire
We decided to construct another drift chamber
  Use 50-μm Ag-coated Al wires without the finishing process (California Fine Wire)
  Recover the original 10-layer configuration. (Existing chamber has 9 layers due to construction schedule.)
  Modify/improve some parts based on the experience of the 1st chamber.
Schedule
  Budget secured (Italy).
  Material procurement started.
  Wiring takes 62 weeks.
  Complete by Mar. 2023.
  → Use it from 2023 run.
Wiring machine re-assembled in INFN-Pisa

## Slide 14: Drift cell configuration
U-layer
V-layer
cathode mesh (40 μm)
cathode wire (50 μm)
In the new CDCH, 50 μm wire will be used also for the cathode mesh.
anode wire (W, 20 μm)

## Slide 15
アルミと銀の境界 ＋ 水分 ＋ 張力 ＝ 腐食による断線
  陰極ワイヤ： 40 or 50 μm 銀コーティングアルミニウムワイヤ
Y. Uchiyama, JPS 2018春
静電力に耐えるために下げられない。
対応済

## Slide 16: Schedule
Sep. | Oct. | Nov. | Dec. | 2022/Jan. | Feb. | Mar.
μ→eγ trigger setup is starting now.
Collect μ→eγ trigger data until Nov.
  This will be the first MEG II physics data
Performance evaluation with πp charge-exchange reaction in Dec.
  Measure energy resolution with full elec.
  Improve method for the measurement of timing resolution.
Perform MPPC annealing in the next spring.
  Annealing was not performed in the last shutdown period.
  Study of the procedure is underway
Trigger setup
Data collection
πp-CEX run
Accelerator shutdown
MPPC annealing

## Slide 17: Summary
The MEG II engineering run is underway,
  Finally with the full readout electronics.
  All the detectors were installed and under commissioning in beam.
  Beamtime continues until Dec.
The main goals are
  To study & understand the LXe MPPC PDE decrease phenomenon and decide the operation scenario.
  To achieve stable operation of CDCH.
  To establish the μ→eγ trigger and begin the physics data collection.
Recently, Kobe University group has officially joined the MEG II collaboration., contributing to the development of upstream RDC with unique RPC technique.

## Slide 18: Dataflow
2×10Gb
2×10Gb
10Gb
Offline cluster
Private network
Archive
PSI network

## Slide 19: Readout electronics
New DAQ/Trigger system
  Use it for all MEG-II detectors in common
  Dense & compact system to cope with increased # of channels.
  Custom multi-functional readout board: WaveDREAM
    Analog FE (programmable shaper & amplifier), SiPM bias-voltage supply, waveform sampling (DRS4), digitization, discriminator, FPGA-based trigger in one module
    No pre-amplifier at detector side
  Synchronization accuracy < 20 ps (over different crate modules)
256 channels/crate
16 channels/module

## Slide 20: Readout electronics
New DAQ/Trigger system
  Use it for all MEG-II detectors in common
  Dense & compact system to cope with increased # of channels.
  Custom multi-functional readout board: WaveDREAM
    Analog FE (programmable shaper & amplifier), SiPM bias-voltage supply, waveform sampling (DRS4), digitization, discriminator, FPGA-based trigger in one module
    No pre-amplifier at detector side
  Synchronization accuracy < 20 ps (over different crate modules)
256 channels/crate
16 channels/module
HV supply
2-stage amplifier
Pole-zero cancellation
Digitization
Trigger
Sync.
SiPM signal waveform digitized at 2.0 GSPS (up to 5 GSPS)
baseline restoration by pole-zero cancellation

## Slide 21: Trigger
More efficient trigger is indispensable.
Trigger logics (basically same as MEG)
Gamma-ray energy threshold
Time coincidence
e–γ direction matching (close to 180°)
Improve by use of higher granularity & better resolution of the detectors
Energy
Hit position
Hit timing
Hit position
Hit timing

## Slide 22: Wire conditioning, aging, & additives
Conditioning (HV training)
  Eliminate dust, contamination, deposit.
  Necessary to apply HV after opening chamber or after aging.
Wire aging (in He:iC4H10)
  Polymer formations by radicals (of HC) created in avalanche.
  Anode aging: Gain decrease (thicker wire), gain non-uniformity along wire.
  Cathode aging: Self-sustain high current and discharge by Malter effect.
Additives to mitigate/recover from aging
  Alcohols (in our case 2-propanol) Reduction of polymerization rate Absorption of UV photons
  O2 Etching (cleaning) of HC-deposit React with HC, becoming stable and volatile Capture e- emitted from Malter effect.
Reduction in gas gain
Reduction of primary e-
+
+
+
+
+
e-
-
cathode
anode
+
+
+
+
+
+
+
+

## Slide 23: Low-mass drift chambers
 | Gas | Cell size | Sense wire | Field wire | 
CLEO II | Ar:C2H6 50:50 | 14 mm | 20-µm Au-W | 110-µm Au-Al, 110-µm Cu/Be | Crimp
BESIII | He:C3H8 60:40 | 12–16.2 mm | 25-µm Au-W | 110-µm Au-Al | Crimp
Belle II | He:C2H6 50:50 | 6–18 mm | 30-µm Au-W | 126-µm Al | Crimp
COMET-Phase I | He:iC4H10 90:10 | 16–16.8 mm | 25-µm Au-W | 126-µm Al | Crimp
KLOE | He:iC4H10 90:10 | 20–30 mm | 25-µm Au-W | 81-µm Ag-Al | Crimp
MEG II | He:iC4H10 90:10 | 6.6–9 mm | 20-µm Au-W | 40-µm Ag-Al | Solder
Other material than Al is not acceptable from the resolution point of view.
Bare Al wire could be a better alternative, but difficulty in soldering. (Naturally coated by Al2O3)
KLOE used same type of wire without any problem for >10 years
  Constructed under 50% R.H., never observed salt formation