Jan 2006

Inspection result of PMT supporting structure

Ryu SAWADA, Satoshi MIHARA

Abstract

We inspected all metallic parts of the PMT supporting structures delivered to Pisa. We report here the inspection result. In addition we summarize required Teflon parts to fix PMTs.

- PMT supporting structures

Details of the PMT supporting structures are summarized in Ref [1]. In this document we call each structure Top, Bottom, Inner, Outer, Upstream, and Downstream structures although different names had been used in Ref [1]. This time we inspected all metallic structure delivered to Pisa INFN. They are Top, Bottom, Outer and Upstream/Downstream. The Upstream and Downstream structures are identical. The Top and Bottom structures are almost same except the shape of holes for assembling.

- Visual Inspection

We performed visual inspection and could not find any fatal mistake in the machining process. Small scratches on the surface will disappear after cleaning and polishing.

- Dimensions

We checked the dimensions of each structure by using a caliper and steal scale. The Outer and Top/Bottom structures were found to be machined correctly. Concerning the Upstream/Downstream structure, we thought that there had been a mistake in the machining process although they were not critical for the construction. However afterwards this was found to be due to our wrong procedure of measurement and it was confirmed by Fabrizio together with the manufacturer that the structure was machined correctly.

- PMT installation test

We performed PMT installation test and checked fixing parts made of Teflon.

  - Outer

We installed 2 PMTs and fixed them by using Teflon parts. We found that all are fine.

  - Top/Bottom

We installed 4 PMTs and fixed them by using Teflon parts. We found that all are fine.

  - Upstream/Downstream

We installed 2 PMTs and fixed them by using Teflon parts. We found in principle the part design is fine. However we came to the conclusion that it is better to modify the parts in order to fix PMTs more stably. Modified design is described later.

- Summary of Teflon parts

| Parts Name | Holder Name | Minimum Amount | Total |
| --- | --- | --- | --- |
| Long Bar I | Outer Outer-Center (at the sides) Top/Bottom (except outermost and innermost rows) | 360 48 162 | 570 |
| Long Bar II | Top/Bottom (in the outermost row) | 18 | 18 |
| Block | Outer-Center (near the center) Top/Bottom (in the innermost raw) | 120 72 | 192 |
| Plate | Upstream/Downstream | 288 | 288 |
| Ring I (6mmx180mm, 2mmt) | Outer Outer-Center (at the sides) Top/Bottom Upstream/Downstream | 180 24 108 288 | 600 |
| Ring II (6mmx180mm, 1mmt) | Outer-Center (near the center) | 30 | 30 |

Dimensions of parts are shown in the followings. As mentioned above, “plate” used to fix PMTs in Upstream/Downstream structures need a minor modification from the previous drawing shown in Ref. [1].

Dimensions of Long bar I

Dimensions of Long bar II

Dimensions of Block

Dimensions of Plate

Dimensions of Ring I and II are

- 6mm x 180mm    2mmt    Ring I

- 6mm x 180mm    1mmt    Ring II

Reference

[1] PMT Fixing Parts for the Xenon Detector, http://meg.web.psi.ch/subprojects/calorimeter/calorimeter.html

# Footnotes

Previous names, “Front (top/bottom)”, “Side”, “Outer”, and “Inner” were quite unpopular and there is no strong reason to stick around them.