## Slide 1: MEG II実験： 実験開始に向けた 2020年の準備状況と予定
Kei Ieki on behalf of MEG II collaboration

## Slide 2: Motivation of search
MEG
MEG II
DeeMe
COMET-I
Mu3e-I
Mu3e-II
COMET-II
Mu2e
μNeN
BSM prediction
(SUSY-seesaw etc.)
Upper limit history
is a good probe of BSM!
Br( ~ in SM + oscillation
e.g. SUSY-seesaw
Experimental sensitivities are already in the region predicted by BSM.
charged Lepton Flavor Violation (cLFV) can never be observed in SM framework.
Br( ~ O(
On the other hand, many well motivated BSMs predicts cLFV

## Slide 3: MEG II experiment
MEG II utilizes world’s highest intensity continuous beam @ PSI.
10
Br
sensitivity
beam rate
@ PSI
Detectors
spectrometer
+ LXe detector
2.3
Improvements:
all resolution ,
efficiency ,
+ new detector
590MeV proton cyclotron @ PSI

## Slide 4: Signal and BG
e
Signal
MEG sensitivity was limited by accidental BG:
52.8 MeV
Same timing
Back to back
Accidental BG
e
from
from
or
Improvement of detector resolution is important!
∝ (beam rate)2

## Slide 5: MEG II detector upgrade
All detectors
upgrade!
Resolution 2 everywhere
efficiency 2
spectrometer: 宇佐見(14aSE-4)
timing counter: 米本(15pSF-4)
BG tagging detector: 恩田(14aSE-2), 大矢(15aSF-1)
LXe detector:
小川(14aSE-3),
小林(15aSE-9),
島田(15pSF-5)
search
(parasite experiment idea)
山本(14aSE-8)

## Slide 6: Overall status
LXe detector
BG tagging detector
drift chamber
timing counter
Readout electronics (WaveDREAM)
Finished construction of all detectors (2018)!  Commissioning is ongoing
Mass production of readout electronics will finish in early 2021.

## Slide 7: timing counter & BG tag detector
timing counter
30 ps already achieved
~8 for signal
timing resolution vs. Nhits
BG () detection probability vs.
BG tagging detector
Successfully identified BG
timing counter & BG tagging detector are ready for physics run.

## Slide 8: LXe detector
upgrade
2-inch PMT 216ch
15mm MPPC 4092ch
Commissioning so far with sources:
17.6 MeV from Li(p,)Be
40~53 MeV from
resolutions: consistent with MC  OK！
resolution: worse than MC (same as MEG)
小川(14aSE-3),
小林(15aSE-9)
Next steps: - Further test with ~55 MeV from (from )
- Radiation damage study  next page
aim: 2 resolution in and

## Slide 9: LXe detector: radiation damage
Accumulation of holes near SiO2-Si interface
 reduction of carrier collection efficiency
Similar phenomena is known for UV photo diode.
Mean PDE vs. time
2017
2018
2019
(~1.31012 photons / day / MPPC)
PDE could become 0% in 70-100 days if it decrease linearly
SiO2
Si
MPPC PDE is found to be decreasing during beam commissioning.
 Likely due to surface damage by VUV scintillation photons.
VUV photons
Surface damage
PDE2019/PDE2018 vs. channel ID
annealed MPPCs
However, we found that PDE can be recovered by annealing (reported by 家城 JPS2020春).  Not a critical problem
Effect on sensitivity:小川(14aSE-3)
Lab test:島田(15pSF-5)

## Slide 10: e+ drift chamber
aim: efficiency,
2~3 resolution in
So far: - Wire breaking problem  due to corrosion accelerated by wire tension & humidity
 Identified & removed weak wires by extra stretching. (spare chamber is also being prepared)  OK !
Al + Ag coated
40 or 50 um (very thin!)
Recent updates:
Corona discharge was causing instable current in 2019
Performance study in MC based on bad S/N situation in 2019
 next pages
increased number of hits
upgrade
Gas: He(90%)+iC4H10(10%),
1728 anode wires (20 W(Au)), 40 or 50 Al(Ag) wire for cathode

## Slide 11: e+ drift chamber: Corona discharge
Stable operation was not possible due to discharges observed at several regions
Whitish deposits seems to be formed, but the mechanism is not understood.
Adding small amount of CO2 or H2O will be tested this year.
“running with an O2 or CO2 additive at high ionization levels can cure a damaged chamber from breakdown problems”

## Slide 12: e+ drift chamber: Performance in bad S/N
Performance of the current readout electronics is worse than what we assumed.
Pre-amp gain: 1/3.7 smaller
Noise (RMS): 2 larger
Example of the waveform in one end of wire
宇佐見(14aSE-4)
Pulse identification algorism is improved to cope with current situation.
Fit the waveform of one end of wire using the waveform observed in the other end
Restriction of analysis time window based on time observed by timing counter
S/N is reduced (~1/10)
(At least the pre-amp gain is expected to be improved)
Target efficiency goal (70%) is still achieved in MC even if the bad S/N situation in 2019 is assumed

## Slide 13: New detector development: RPC
BG
Existing BG tagging detector
RPC
Detector to identify main BG source by tagging low energy .
Downstream detector is already installed.
New upstream detector  RPC
It must be placed in 28 MeV/c beam.
 Extremely low material (<0.1%) is required!
 Resistive Plate Chamber (RPC) with Diamond-Like Carbon (DLC) electrodes
DLC
大矢(15aSF-1)
~300 um gap
Freon based gas
Good performance achieved with prototype ! (90Sr): - ~90% efficiency with 4 layers - ~250 ps time resolution
Next step: high rate capability test

## Slide 14: Muon beam test 2020
Main goals:
- LXe performance estimation with ~55 MeV from
- Establish stable operation of drift chamber
Current situation:
- Beam time (& man-power) is reduced due to COVID-19, but we still have time in Oct. ~ Nov.
- In 2019, Beam Transport Solenoid coil (for momentum adjustment and focusing) broke, but repairing work is expected to finish soon.

## Slide 15: Summary
MEG II experiment will search with 10 better sensitivity than MEG.
Construction of all the detectors is completed, and commissioning is ongoing. Full readout electronics are expected to become ready in early 2021.
We will perform a beam test in the end of 2020, aiming at:
  Stable operation of drift chamber
  Performance evaluation of LXe detector with ~55 MeV .

## Slide 16: Backup slides

## Slide 19: drift chamber
1728 anode wires in 6-8mm interval, 9 layers  many hits per track  good resolution ( ~ 130 keV, ~ 5 mrad expected)
No extra material between timing counter  efficiency 2
Cylindrical stereo wire chamber (stereo angle: )
Low mass ( X0 along track) low multiple scattering  good resolution Gas: He(90%)+iC4H10(10%), Wire: 20 W(Au) for anode, 40 or 50 Al(Ag) for cathode
Example of signal

## Slide 20: timing counter
Fast plastic scintillator + SiPM
Increased segmentation  many hits per track
 good resolution
= 38.5 ps already achieved
6 SiPMs series connection
~8 for signal
series connection makes the waveform sharp
To improve time resolution:
- Use many SiPMs  high light yield
- Connect them in series  less readout ch, short risetime

## Slide 21: LXe detector
Uniformity of sensor coverage and granularity improved!  Energy and position resolution improves by factor of 2 in MC
Energy resolution
2%  0.7~1.5%
Example of BG event in beam run
(part of the detector was readout)